## Slide 1: Sensing
Instructor: Deepak Gangadharan

## Slide 2: Sensor – Energy Converter
A sensor may incorporate several transducers. The last part is a direct sensor producing electrical output
Example: A chemical sensor produces electrical signal in response to a chemical reaction. It may have two parts: first one converts the energy of a chemical reaction to heat (transducer) and the other part (thermopile) converts the heat into an electrical signal
Direct sensor and Indirect Sensor
Source: https://www.philadelphia.edu.jo/academics/kaubaidy/uploads/Sensor-Lect2.pdf

## Slide 3: Types of Sensors
Output
Analog
Digital
Datatype
Scalar
Vector
Intermediate Stages
Direct sensor
Indirect sensor

## Slide 4: Types of Sensors
Direct Sensor: Converts a stimulus into an electrical signal or modifies an electrical signal by using an appropriate physical effect Example: Thermocouple
Indirect Sensor: Includes one or more transducers for multiple conversion steps before a direct sensor generates an electrical output

## Slide 5: Types of Sensors
Output
Analog
Digital
Datatype
Scalar
Vector
Power Requirement
Active
Passive
Intermediate Stages
Direct sensor
Indirect sensor

## Slide 6: Types of Sensors
Passive Sensor: Does not need any additional energy source and directly generates an electrical signal in response to external stimulus. Most passive sensors are direct sensors as defined earlier. Example: Thermocouple, photodiode, piezoelectric sensor
Active Sensor: Requires external power for its operation, which is called an excitation signal. Example: LiDAR, GPS, infrared sensor

## Slide 7: Types of Sensors
Output
Analog
Digital
Datatype
Scalar
Vector
Power Requirement
Active
Passive
Intermediate Stages
Direct sensor
Indirect sensor
Reference
Absolute
Relative

## Slide 8: Types of Sensors
Absolute Sensor: Detects a stimulus in reference to an absolute physical scale that is independent of the measurement conditions Example: Thermistor
Relative Sensor: Stimulus is sensed with respect to a fixed or variable reference that is not an absolute value independent of measurement conditions Example: Thermocouple

## Slide 9: Types of Sensors
Output
Analog
Digital
Datatype
Scalar
Vector
Power Requirement
Active
Passive
Intermediate Stages
Direct sensor
Indirect sensor
Reference
Absolute
Relative
Stimulus contact
Contact
Non-contact

## Slide 10: Types of Sensors
Contact sensor: Requires physical contact with the stimulus Example: strain gauges, temperature sensors
Non-contact sensor: Requires no physical contact Example: optical and magnetic sensors

## Slide 11: Sensor Characteristics
Static Characteristics
  Range and Span
  Accuracy
  Resolution
  Precision
  Errors
  Sensitivity
  Linearity
  Hysterisis
Dynamic Characteristics

## Slide 12: Range and Span
Range Minimum and Maximum value of a physical quantity that a sensor can measure Example: A Resistance Temperature Detector (RTD) for the measurement of temperature has a range of -200 to 800˚C
Span Difference between maximum and minimum values of input measured In the above example, span of RTD = 800 – (-200) = 1000˚C

## Slide 13: Accuracy and Resolution
Accuracy is the capacity of a sensor to give results close to the TRUE VALUE of the measured quantity
  Measured by absolute and relative errors ABSOLUTE ERROR = RESULT – TRUE VALUE RELATIVE ERROR = ABSOLUTE ERROR / TRUE VALUE
Resolution is the minimal change of the input necessary to produce a detectable change at the output

## Slide 14: Precision
Capacity of a sensor to give same reading when repetitively measuring the same quantity under the same prescribed conditions
Source: https://www.electrical4u.com/characteristics-of-sensors/

## Slide 15: Errors
Systematic Errors Due to interfering or modifying variables (e.g., temperature), loading, attenuation, etc.
Random Errors A signal that carries no information such as environmental noise
Source: https://www.philadelphia.edu.jo/academics/kaubaidy/uploads/Sensor-Lect2.pdf

## Slide 16: Sensitivity
Ratio of change in output to change in input. If is the output quantity in response to input , then sensitivity can be expressed as
It is also the slope of the calibration curve

## Slide 17: Linearity
Maximum deviation between the measured values of a sensor from ideal curve
Source: https://appmeas.co.uk/resources/pressure-measurement-notes/linearity-or-nonlinearity/

## Slide 18: Hysteresis
Difference in output for same input when the input is reached at from different trajectories
Source: https://www.electrical4u.com/characteristics-of-sensors/

## Slide 19: Dynamic Characteristics
Sensor response to a variable input is different from what is seen when the input signals are constant (described by static characteristics)
Dynamic Characteristics are determined by analyzing the response of the sensor to a family of variable input waveforms
Source: https://www.philadelphia.edu.jo/academics/kaubaidy/uploads/Sensor-Lect2.pdf

## Slide 20: DHT11 sensor
Source: https://components101.com/dht11-temperature-sensor
Basic low cost digital temperature and humidity sensor
Uses capacitive humidity sensor and a thermistor to measure the surrounding air and outputs a digital signal on the data pin
Easy to use, only downside being new data can be received only once in every 2 secs
Consists of a humidity sensing component, a NTC temperature sensor (thermistor) and an IC on the back side.
Source: http://robocraft.ru/files/datasheet/DHT11.pdf

## Slide 21: DHT11 working principle
A humidity sensing component is used which has two electrodes and a moisture holding substrate between them
Change in humidity  Conductivity of substrate changes or the resistance between the electrodes changes
IC measures and processes this change and makes it ready to read
Source: https://howtomechatronics.com/tutorials/arduino/dht11-dht22-sensors-temperature-and-humidity-tutorial-using-arduino/

## Slide 22: DHT11 working principle
A thermistor is a variable resistor that changes its resistance with changes in temperature
The term NTC refers to “negative temperature coefficient”  resistance decreases with increase of temperature
Source: https://howtomechatronics.com/tutorials/arduino/dht11-dht22-sensors-temperature-and-humidity-tutorial-using-arduino/

## Slide 23: LDR sensor
A Light Dependent Resistor (LDR) or a photoresistor is a device made up of high resistance semiconductor material
Passive sensor
Resistance changes with the change in light intensity
Preferred for outdoor lighting and automatic street lighting circuits
Source: https://www.elprocus.com/ldr-light-dependent-resistor-circuit-and-working/

## Slide 24: Smart Home Sensors
Source: https://www.alibaba.com/product-detail/Smart-Home-2-4G-ZigBee-Indoor_60643366019.html

## Slide 25: Sensors in a modern car
Source: https://carfromjapan.com/article/car-maintenance/types-of-sensors-used-in-automobile-engine/

## Slide 26
Thank You